## Slide 1: CS361: Computer Architecture
CS324 Computer Architecture 1
Data-level Parallelism..
Floating-point Arithmetic Pipelines

## Slide 2: FLOATING-POINT REPRESENTATION
The floating-point representation of a number has two parts.
  The first part represents a signed, fixed-point number (or an integer)
called the mantissa.
  The second part designates the position of the decimal (or binary) point and is called the exponent.
Example floating point representation of decimal numbers:
– The value of the exponent indicates that the actual position of the decimal point is four positions to the right of the indicated decimal point in the fraction (6132789)
– The value of the exponent indicates that the actual position of the decimal point is four positions to the left of the indicated decimal point in the integer (12345)
6132.789 = | Mantissa | Exponent
 | 6132789 | +4
1.2345 = | Mantissa | Exponent
 | 12345 | -4

## Slide 3
FLOATING POINT ADDITION
How to add the following two numbers?
X = 0.97 * 102 Y = 0.81 * 101
Answer: Through the following four steps
  Compare the exponents
  Align the mantissa/exponent in Y
  Add or subtract the mantissas
  Normalize the result (so that it has a fraction with a
nonzero first digit)

## Slide 4: FLOATING POINT ADDITION
Step1: Compare the exponents
2 > 1, so align Y
  In the first stage, we compare the exponents and determine that the exponent of X is one greater than the exponent of Y.
Step 2: Align the mantissa/exponent
Y = .081 * 102
  In step 2 we choose the exponent of Y to be 2. Next we align the
mantissa by shifting the mantissa of Y one position to the right:
Y = .81 * 101 as Y = .081 * 102.
  Note that this does not change the value of Y, but only its
representation.

## Slide 5: FLOATING POINT ADDITION
Now that the mantissas are aligned, i.e. both numbers have the same exponent, we can add the mantissas.
Step 3: Add the mantissas
0.97 + .081 = 1.051
Step 4: Normalize the result
X + Y = 1.051 * 102 = .1051 * 103
  The result of the addition, 1.051 * 102, is not in normal form.
  The sum is adjusted by normalizing the result so that it has a fraction with a nonzero first digit. This is done by shifting the mantissa once to the right and incrementing the exponent by one to obtain the normalized sum. This converts 1.051 * 102 to .1051 * 103

## Slide 6: FLOATING POINT ADDITION
A floating point adder-subtractor circuit follows the same 4 steps for addition and subtration.
As an example of a “pipelined” arithmetic unit we consider a floating point adder-subtractor
We will see that the 4 manual steps will form the 4 segments of the pipeline.

## Slide 7: FLOATING-POINT ARITHMETIC PIPELINE
Seg 1: Compare the exponents
Seg 2: Choose exp. & Align mantissa
Seg 3: Add/sub the mantissa
Seg 4: Normalize the result
Floating-point adder-subtractor
X = A x 10a Y = B x 10b
R
Compare exponents
by subtraction
b
R
Choose exponent
Exponents a
R
B
Align mantissa
Mantissas A
Difference
R
Add or subtract
mantissas
R
Normalize result
R
Adjust exponent
R
Segment 1:
Segment 2:
Segment 3:
Segment 4:

## Slide 8: FLOATING-POINT ARITHMETIC PIPELINE
Seg 1: The two exponents are subtracted to obtain 3 - 2 = 1.
Seg 2: Shifts the mantissa of Y to the right to obtain
Y = 0.08200 X 103
Seg 3: Adds the two mantissas
Z = 1.0324 X 103
Seg 4: The sum is adjusted by normalizing the result
Z = 0.10324 X 104
Floating-point adder-subtractor
X = 0.9504 X 103
Y = 0.8200 X 102
R
Compare exponents
by subtraction
b
R
Choose exponent
Exponents a
R
B
Align mantissa
Mantissas A
Difference
R
Add or subtract
mantissas
R
Normalize result
R
Adjust exponent
R
Segment 1:
Segment 2:
Segment 3:
Segment 4: