## Slide 1: CS361: Computer Architecture
CS324 Computer Architecture 1
Reading Sections: : Computer Organization & Design: HW/SW Interface, 5th Edition: Section 5.1
Computer Architecture: A Quantitative Approach, Sixth Edition, Section 2.1
  Principle of Locality
  Memory Hierarchy
    Instrcutor:Waheed Ahmad
Week 6-7: Memory Performance

## Slide 2: THE MEMORY ANALOGY
The memory system is a major factor in determining performance.
– The library analogy
» Having several books on the desk in front of you saves time compared to having only one book there and constantly having to go back to the shelves to return it and take out another.

## Slide 3: THE MEMORY ANALOGY
Just as you did not need to access all the books in the library at once, a program does not access all of its code or data at once.
You have used limited desk space to quickly search material and write the report.
  It would be impossible for you to fit all the library books on your desk
and still find what you wanted quickly.
  A computer uses limited (but fast-access) memory to support fast processing.
  Compare the library analogy with the “Principle of locality”

## Slide 4: PRINCIPLE OF LOCALITY
The Principle of locality states that a processor accesses relatively small portions of programs at any instant of time
  just as you accessed a very small portion of the library’s collection.
  A program spends 90% of its execution time in only 10% of the code.
  This principle also applies to data accesses, though not as strongly as to code accesses.

## Slide 5: RECALL
A memory hierarchy consists of multiple levels of memory
with different speeds and sizes.
Cache
Main Memory
Auxiliary memory
As the distance from the processor increases, so does the size

## Slide 6: MEMORY HIERARCHY
Why do we need memory hierarchy?
To obtain the highest possible access speed while minimizing the total cost of the memory system
– Faster memories are more expensive per bit than the slower memories and thus are smaller
To take advantage of the “Principle of locality” by
implementing the memory of a computer as a hierarchy
Performance is the major reason for having a memory hierarchy

## Slide 7: MEMORY HIERARCHY
Why do we need memory hierarchy?
To obtain the highest possible access speed while minimizing the total cost of the memory system
– The faster memories are more expensive per bit than the slower
memories and thus are smaller
To take advantage of the “principle of locality” by implementing the memory of a computer as a memory hierarchy
Performance is the major reason for having a memory hierarchy

## Slide 8: MEMORY HIERARCHY
As the distance from the processor increases, so does the size

## Slide 9: MEMORY HIERARCHY

## Slide 10: MEMORY HIERARCHY
Why do we need memory hierarchy?
To obtain the highest possible access speed while minimizing the total cost of the memory system
– The faster memories are more expensive per bit than the slower
memories and thus are smaller
To take advantage of the “principle of locality” by implementing the memory of a computer as a memory hierarchy
Performance is the major reason for having a memory hierarchy

## Slide 11: MEMORY HIERARCHY
As the distance from the processor increases, so does the size

## Slide 12: MEMORY HIERARCHY

## Slide 13: MEMORY TECHNOLOGIES
Three primary technologies used in building memory hierarchies
1. Cache memory: At the level closest to the processor. Cache use SRAM (static random access memory)
2. Main memory is implemented using DRAM (dynamic random access memory) technology
3. Auxiliary memory: Flash memory and/or Magnetic disk
Cache
Main Memory
Auxiliary memory
The access time and price per bit vary among these technologies
Memory technology | Typical access time (ns) | $ per GB
SRAM semiconductor memory | 0.5 ─ 2.5 | 500 ─ 1000
DRAM semiconductor memory | 50 ─ 70 | 10 ─ 20
Flash semiconductor memory | 5,000 ─ 50,000 | 0.75 ─ 1.0
Magnetic disk | 5,000,000 ─ 20,000,000 | 0.05 ─ 0.10

## Slide 14: PROCESSOR VS MEMORY PERFORMANCE IMPROVEMENT

## Slide 15: DATA HIERARCHY
The data is similarly hierarchical: A level closer to the processor is generally a subset of any level further away, and all the data is stored at the lowest level.
Data is copied between only two adjacent levels of memory at a time.
The upper level
  The one closer to the processor
  smaller and faster but more expensive
Lower level
  Larger but slower and less expensive

## Slide 16: DATA HIERARCHY
Block
  The minimum unit of information present in a cache
  For instance, one book in the analogy considered
If the data requested by the processor appears in some block in the upper level, this is called a hit
If the data is not found in the upper level, the request is
called a miss

## Slide 17: DATA HIERARCHY
Since performance is the major reason for having a memory hierarchy, the time to service hits and misses is important.
Hit time is the time to access the upper level of the memory hierarchy, which includes the time needed to determine whether the access is a hit or a miss
  That is, the time needed to look through the books on the desk
Miss penalty is the time to replace a block in the upper level with the corresponding block from the lower level, plus the time to deliver this block to the processor
  That is, in case of a miss, the time to get the required book from the shelf and place it on the desk

## Slide 18: TYPES OF LOCALITY
Temporal locality (locality in time)
Spatial locality (locality in space)

## Slide 19: TEMPORAL LOCALITY
i.e. locality in time
  If a data collection is used, it will tend to be used again soon.
  For example, if you recently brought a book to your desk to look at, you will probably need to look at it again soon.
  Similarly, in programs containing loops, the instructions and data are likely to be accessed repeatedly, showing high amounts of temporal locality

## Slide 20: SPATIAL LOCALITY
i.e. locality in space
  If an item is used, the items whose addresses are close-by will also tend to be used soon.
  Librarians stock books on the same topic together on the same shelfs to increase spatial locality
  Since instructions are normally accessed sequentially, programs also
show high spatial locality
  Accesses to data also exhibit a natural spatial locality. For example, sequential accesses to elements of an array or a record will naturally have high degrees of spatial locality.

## Slide 21: RECAP: WHAT IS CACHE?
A secret store of valuables or money
  Compare with the library analogy.
In computing, cache was the name chosen to represent the level of memory hierarch between the CPU and main memory in the early commercial computers, in order to:
  Take advantage of the “Principal of locality”.
  Optimize data transfers.
Let’s look at the working of a simple cache.

## Slide 22: CACHE BASICS
A processor will always use the main memory address to find an item (instruction or operand), even if a cache exists in the system.
This means that the main memory address of an item should
also be stored inside in the cache.

## Slide 23: A SIMPLE CACHE
Consider a cache in which the processor requests are each one word and the blocks also consist of a single word.
– This reference causes a miss that forces the cache to fetch Xn from
the main memory and insert it into the cache.
Questions:
  How do we know if the requested data item is in the cache?
  If it is, how do we find it?

## Slide 24: DIRECT MAPPED CACHE
If each memory word (block) can go in exactly one place in the cache, then it becomes straightforward to find the word in the cache.
  This is called direct mapping
Direct-mapped cache
  A cache structure in which each memory location is mapped to exactly one location in the cache, based on the address of the word in the main memory.
  This mapping between addresses and cache locations is used to find
a block.

## Slide 25: DIRECT MAPPED CACHE
Cache size: n words, for n = 2,4,8,16...
log2 (n) lower bits of address are used as the cache index field.
The remaining upper bits of address are used in the tag field.
CACHE |  | 
Tag | Index | Data

## Slide 26: DIRECT MAPPED CACHE
The lower order log2 (8) = 3 bits are used as cache index.
Thus, 00001, 01001, 10001, and 11001 map to entry 001 of the cache,
While 00101,01101, 10101 and 11101 map to entry 101 of the cache, and so on.

## Slide 27: DIRECT MAPPED CACHE
To find a word in cache: (word address in main memory) mod n => index
If its a hit, the tag field is used to uniquely identify the requested word.
The index content of a cache word, together with the tag content of that word, uniquely specify the memory address of the requested word contained in cache.
Let’s consider an example.
CACHE |  | 
Tag | Index | Data

## Slide 28: ACCESSING A CACHE
Cache
Tag
Index
Data
10
110
M [10110]
Sequence of memory references |  | 
Address of reference | Assigned cache Hit or miss block | 
10110
10110 mod 8 = 110
miss
000
001
010
011
100
101
110
111
An empty 8-block Cache

## Slide 29: ACCESSING A CACHE
Cache |  | 
Tag | Index | Data
 | 000 | 
 | 001 | 
11 | 010 | M [11010]
 | 011 | 
 | 100 | 
 | 101 | 
10 | 110 | M [10110]
 | 111 | 
Sequence of memory references |  | 
Address of reference | Assigned cache block | Hit or miss
10110 | 10110 mod 8 = 110 | miss
11010
11010 mod 8 = 010
miss

## Slide 30: ACCESSING A CACHE
Cache |  | 
Tag | Index | Data
 | 000 | 
 | 001 | 
11 | 010 | M [11010]
 | 011 | 
 | 100 | 
 | 101 | 
10 | 110 | M [10110]
 | 111 | 
Sequence of memory references |  | 
Address of reference | Assigned cache block | Hit or miss
10110 | 10110 mod 8 = 110 | miss
11010 | 11010 mod 8 = 010 | miss
10110 | 10110 mod 8 = 110 | hit

## Slide 31: ACCESSING A CACHE
Cache |  | 
Tag | Index | Data
 | 000 | 
 | 001 | 
11 | 010 | M [11010]
 | 011 | 
 | 100 | 
 | 101 | 
10 | 110 | M [10110]
 | 111 | 
Sequence of memory references |  | 
Address of reference | Assigned cache block | Hit or miss
10110 | 10110 mod 8 = 110 | miss
11010 | 11010 mod 8 = 010 | miss
10110 | 10110 mod 8 = 110 | hit
11010
11010 mod 8 = 010
hit

## Slide 32: ACCESSING A CACHE
Cache |  | 
Tag | Index | Data
10 | 000 | M [10000]
 | 001 | 
11 | 010 | M [11010]
 | 011 | 
 | 100 | 
 | 101 | 
10 | 110 | M [10110]
 | 111 | 
Sequence of memory references |  | 
Address of reference | Assigned cache block | Hit or miss
10110 | 10110 mod 8 = 110 | miss
11010 | 11010 mod 8 = 010 | miss
10110 | 10110 mod 8 = 110 | hit
11010 | 11010 mod 8 = 010 | hit
10000 | 10000 mod 8 = 000 | miss

## Slide 33: ACCESSING A CACHE
00
M[00011]
Cache |  | 
Tag | Index | Data
10 | 000 | M [10000]
 | 001 | 
11 | 010 | M [11010]
 | 011 | 
 | 100 | 
 | 101 | 
10 | 110 | M [10110]
 | 111 | 
00011
00011 mod 8 = 011
Sequence of memory references |  | 
Address of reference | Assigned cache block | Hit or miss
10110 | 10110 mod 8 = 110 | miss
11010 | 11010 mod 8 = 010 | miss
10110 | 10110 mod 8 = 110 | hit
11010 | 11010 mod 8 = 010 | hit
10000 | 10000 mod 8 = 000 | miss
 |  | miss

## Slide 34: ACCESSING A CACHE
Cache |  | 
Tag | Index | Data
10 | 000 | M [10000]
 | 001 | 
11 | 010 | M [11010]
00 | 011 | M[00011]
100 |  | 
101 |  | 
10 | 110 | M [10110]
111 |  | 
Sequence of memory references |  | 
Address of reference | Assigned cache block | Hit or miss
10110 | 10110 mod 8 = 110 | miss
11010 | 11010 mod 8 = 010 | miss
10110 | 10110 mod 8 = 110 | hit
11010 | 11010 mod 8 = 010 | hit
10000 | 10000 mod 8 = 000 | miss
00011 | 00011 mod 8 = 011 | miss
10000 | 10000 mod 8 = 000 | hit

## Slide 35: ACCESSING A CACHE
11
M [11010]
Sequence of memory references |  | 
Address of reference | Assigned cache block | Hit or miss
10110 | 10110 mod 8 = 110 | miss
11010 | 11010 mod 8 = 010 | miss
10110 | 10110 mod 8 = 110 | hit
11010 | 11010 mod 8 = 010 | hit
10000 | 10000 mod 8 = 000 | miss
00011 | 00011 mod 8 = 011 | miss
10000 | 10000 mod 8 = 000 | hit
10010
10010 mod 8 = 010
miss
Cache |  |  |  |  | 
 | Tag | Index |  | Data | 
 | 10 | 000 |  | M [10000] | 
 |  | 001 |  |  | 
 | 10 | 010 |  | M [10010] | 
 | 00 | 011 |  | M[00011] | 
 |  | 100 |  |  | 
 |  | 101 |  |  | 
 | 10 | 110 |  | M [10110] | 
 |  | 111 |  |  | 

## Slide 36: ACCESSING A CACHE
Cache |  | 
Tag | Index | Data
10 | 000 | M [10000]
 | 001 | 
10 | 010 | M [11010]
00 | 011 | M[00011]
100 |  | 
101 |  | 
10 | 110 | M [10110]
111 |  | 
Sequence of memory references |  | 
Address of reference | Assigned cache block | Hit or miss
10110 | 10110 mod 8 = 110 | miss
11010 | 11010 mod 8 = 010 | miss
10110 | 10110 mod 8 = 110 | hit
11010 | 11010 mod 8 = 010 | hit
10000 | 10000 mod 8 = 000 | miss
00011 | 00011 mod 8 = 011 | miss
10000 | 10000 mod 8 = 000 | hit
10010 | 10010 mod 8 = 010 | miss
10000 | 10000 mod 8 = 000 | hit

## Slide 38: Class Practice
Address of Reference | Assigned Cache Block | Hit or Miss
10101 |  | 
11001 |  | 
10101 |  | 
00101 |  | 
10001 |  | 
10101 |  |