## Slide 1: CS361: Computer Architecture
CS324 Computer Architecture 1
Instruction-level Parallelism
Pipelining: Practical Speedup
Pipelining: Basic Performance Issues
Book Computer Architecture: A Quantitative Approach, Sixth Edition, Section C.1 – C2
Reference Computer System Architecture, 3rd Edition: Section 9.2

## Slide 2: WHAT IS THE “PRACTICALLY” POSSIBLE SPEEDUP?
Although pipelining speeds up the execution of tasks as opposed to a unpipelined execution, the “maximum theoretical speed” is never fully achieved in practice due to basic performance issues in pipelining.

## Slide 3: BASIC PERFORMANCE ISSUES IN PIPELINING
Due to the following reasons a pipeline cannot operate at its
maximum theoretical rate.
  Pipelining Overhead
  Instruction throughput Versus Instruction execution time

## Slide 4: PIPELINING OVERHEAD
Circuit Overhead: An unpipelined circuit does not have the same time delay as that of an equivalent pipelined circuit.
» Time delay: logic gates do not operate instantaneously because of the way transistor switching works at the physical level; there is a small delay between when the inputs are supplied and when the output is produced (also called propagation time)
» Many of the intermediate registers in a pipeline are not needed in an unpipelined circuit, which is constructed entirely as a single-unit combinational circuit.
Imbalance among the pipe stages: Different segments may take different times to complete their microoperation(s).
» The clock cycle must be chosen to equal the time delay of the segment with the maximum propagation time. This causes all other segments to waste time while waiting for the next clock which reduces performance.

## Slide 5: INSTRUCTION THROUGHPUT VS. INSTRUCTION LATENCY
Pipelining increases the instruction throughput (i.e. the number of instructions completed per unit time)
But the increased throughput does not decrease the execution time of an individual instruction.
  In fact, pipelining slightly increases the execution time of each
instruction due to “pipelining overhead”.
The increase in instruction throughput means that a program runs faster and has a lower “overall” execution time, due to the overlapped instruction execution in pipelining. However, no single instruction can run faster than it could in an unpipelined execution.
  Through pipelining, we don’t speed up execution of individual instructions; rather, we overlap computations (i.e. perform more instructions simultaneously), in order to generate more results in less time.
Pipelining can be thought of as decreasing the CPI

## Slide 6: SPEEDUP SCENARIO-I
Un-pipelined execution of the task will take 7 x 3 clock cycles to complete
  Assuming the clock cycle time is 1ns, then according to the CPU time formula
  CPU time = number of instructions x CPI x clock cycle time
= 7 x 3 x 1ns = 21ns
Pipelined execution takes only 9 clock cycles to complete as shown in the table above (or 9ns assuming clock cycle time = 1 ns)
Speedup = 21ns / 9ns = 2.33
Clock Pulse Number | Segment 1 |  | Segment 2 |  | Segment 3
 | R1 | R2 | R3 | R4 | R5
1 | A1 | B1 |  |  | 
2 | A2 | B2 | A1 * B1 | C1 | 
3 | A3 | B3 | A2 * B2 | C2 | A1 * B1 + C1
4 | A4 | B4 | A3 * B3 | C3 | A2 * B2 + C2
5 | A5 | B5 | A4 * B4 | C4 | A3 * B3 + C3
6 | A6 | B6 | A5 * B5 | C5 | A4 * B4 + C4
7 | A7 | B7 | A6 * B6 | C6 | A5 * B5 + C5
8 |  |  | A7 * B7 | C7 | A6 * B6 + C6
9 |  |  |  |  | A7 * B7 + C7
Operations in each pipeline stage

## Slide 7: SPEEDUP SCENARIO-I
n: Number of instructions to be executed
(n = 7 in scenario-I)
Conventional Machine (un-pipelined case)
tn: Time required to complete each instruction
(tn = CPI x clock cycle time = 3 x 1ns = 3ns in scenario-I)
Then n instructions will be completed in Timeunpipe = n * tn
(Timeunpipe
= 7 x 3ns = 21ns in scenario-I)
Pipelined Machine (with k segments) (k=3 in scenario-I)
tp: Clock cycle time to complete each segment (1ns in scenario-I)
The first instruction requires a time equal to k.tp to complete its execution (3ns in scenario-I)
The remaining (n – 1) instructions emerge from the pipe at the rate of one instruction per clock cycle, so all remaining instructions will complete in time (n – 1)tp (6ns in scenario-I)
Therefore, n tasks using a k-segment pipeline will complete in: Timepipe = (k + n – 1) tp
(3+6= 9ns in scenario-I)
pipe
Timeunpipe
Time
ntn
kn1tp
Speedup  
(21/ 9= 2.33 times in scenario-I)

## Slide 8: NUMERICAL EXAMPLE
Consider again Scenario-I (n=7, CPI=3, clock cycle time = 1ns).
The theoretical speedup that this pipeline can achieve is
What will be the actual speedup if the pipelining adds an
overhead of 0.3 ns to each instruction execution?
Speedup 
tn tp
 k  3

## Slide 9
It will affect the pipelined time
tpactual​=Ideal segment time+Overhead
tpactual​=1 ns+0.3 ns=1.3 ns.
Timepipe,actual​=(3+7−1)×1.3 ns
Speedupactual​=21 ns/11.7​≈1.79

## Slide 10: PIPELINING HAZARDS
There are situations, called hazards, that cause an instruction pipeline to deviate from its normal operation and reduce the speedup.
Avoiding a hazard often requires that some instructions in the pipeline be allowed to proceed while others are delayed (or stalled).
  Hazards in a pipeline may make it necessary to stall a pipeline.
  A stall is the waste of a clock cycle caused due to a hazard.

## Slide 12: TYPE OF HAZARDS
Three major hazards:
  Structural hazards (also called resource conflicts)
  Data hazards (also called data dependency)
  Control hazards (also called branch difficulties)

## Slide 13: STRUCTURAL HAZARDS
Structural hazards are caused by resource conflicts.
  Resource conflicts are caused by access to memory by two segments at the same time.
If two or more instructions cannot be overlapped in a pipeline because of a resource conflict, the pipeline is said to have a structural hazard.
  Some pipelined processors have a single memory shared for fetching both data and instructions. As a result, when an instruction contains a data reference, it may conflict with the instruction reference for a later instruction.
  Lets consider an example.

## Slide 14: EXAMPLE OF A STRUCTURAL HAZARD
Cloc
Instructions
Consider a 4-Segment Pipeline
FI: Fetch an instruction from memory
DA: Decode the instruction and calculate
the effective address of the operand
FO: Fetch the operand
EX: Execute the instruction
Assume that the processor does not have separate instruction and data memories so that the operation in FI and FO cannot be overlapped.
k Cycles |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | 1 | FI | DA | FO | EX |  |  |  |  |  |  |  |  | 
2 3 |  |  | FI | DA | FO | EX |  |  |  |  |  |  |  | 
 |  |  |  | stall | stall | FI | DA | FO | EX |  |  |  |  | 
4 |  |  |  |  |  |  | FI | DA | FO | EX |  |  |  | 
5 |  |  |  |  |  |  |  | stall | stall | FI | DA | FO | EX | 
6 |  |  |  |  |  |  |  |  |  |  | FI | DA | FO | EX
7 |  |  |  |  |  |  |  |  |  |  |  | stall | stall | …

## Slide 15: HOW TO AVOID STRUCTURAL HAZARDS?
Structural hazards can be avoided by using separate memories for instruction and data with separate memory buses.
However, providing separate instruction and data memories is too expensive.
– If a structural hazard is rare, it may be ignored to reduce the cost of
manufacturing a pipelined processor.

## Slide 16: DATA HAZARDS
A data hazard occurs when the execution of an instruction depends on the result of a previous instruction.
An instruction scheduled to be executed in the pipeline requires the result of a previous instruction, which is not yet available.
Lets consider an example.

## Slide 17: EXAMPLE OF A DATA HAZARD
Instruction-1 | ADD | R1, R2, R3
Instruction-2 | SUB | R4, R1, R5
Instruction-3 | AND | R6, R1, R7
1 | 2 | 3 | 4 | 5 | 6 | 7
FI | DA | FO | EX | WB |  | 
 | FI | DA | FO | EX | WB | 
 |  | FI | DA | FO | EX | WB
ADD R1, R2, R3
SUB R4, R1, R5
AND R6, R1, R7
The result of instruction-1 (ADDition) is stored in R1 at the end of 5th clock cycle; whereas R1 is fetched by instruction-2 in 4th clock cycle and by instruction-3 at the beginning of the 5th clock cycle.
– The results is that Instruction-2 and instruction-3 will fetch wrong value of R1.
This situation leads to a data hazard
R1

## Slide 18: Simulation Example
  add x3, x0, x0
sub x5, x3, x4
add x6, x0, x0
add x7, x0, x0

## Slide 19: How can we fix it?
Ideas?

## Slide 20: Solution 1: Make the compiler deal with it.
EX
Deco
de
Fetch
Mem
Write
back

## Slide 21: Solution 2: Stall
When you need a value that is not ready, “stall”
  Suspend the execution of the executing instruction
  and those that follow.
  This introduces a pipeline “bubble.” A bubble is a lack of
work to do. It moves through the pipeline like an instruction.
EX
D
d
eco
e
Fetch
Mem
ite ck
Wr
ba
add $s0, $t0, $t1
Fetch
sub $t2, $s0, $t3
Cycles
EX
D
d
eco
e
Mem
ite ck
Wr
ba
Stall

## Slide 22: Stalling the pipeline
Freeze all pipeline stages before the stage where
the hazard occurred.
  Disable the PC update
Disable the pipeline registers
•
This essentially equivalent to always inserting a
nop when a hazard exists

## Slide 23: Solution 3: Bypassing/Forwarding
Data values are computed in Ex and Mem but
“publicized in write back”
The data exists! We should use it.
EX
D
d
eco
e
Fetch
Mem
ite ck
Wr
ba
results known
Results "published" to registers
inputs are needed

## Slide 24: Bypassing or Forwarding
Take the values, where ever they are
•
EX
D
d
eco
e
Fetch
Mem
ite ck
Wr
ba
add $s0, $t0, $t1
EX
D
d
eco
e
Fetch
Mem
ite ck
Wr
ba
sub $t2, $s0, $t3
Cycles

## Slide 25: Forwarding Paths
EX
D
d
eco
e
Fetch
Mem
ite ck
Wr
ba
add $s0, $t0, $t1
EX
D
d
eco
e
Fetch
Mem
ite ck
Wr
ba
sub $t2, $s0, $t3
Cycles
EX
D
d
eco
e
Fetch
Mem
ite ck
Wr
ba
EX
D
d
eco
e
Fetch
Mem
ite ck
Wr
ba
sub $t2, $s0, $t3
sub $t2, $s0, $t3

## Slide 26: What can we do?
Punt to the compiler
  Easy enough.
  Will work.
Same dangers apply as before.
•
Always stall.
Forward when possible, stall otherwise
Here the compiler still has leverage
If the compiler can’t fix it, the hardware will stall
26

## Slide 27
Home task: Book Section C-2

## Slide 28: BRANCH HAZARDS
A branch (or interrupt) instruction can be conditional or unconditional.
  An unconditional branch always alters the sequential program flow by loading the program counter (PC) with the target address.
  In a conditional branch, the control selects the target instruction if the condition is satisfied or the next sequential instruction if the condition is not satisfied.
» Branch target address is not known until the branch instruction is executed.
One of the major problems in operating an instruction pipeline is the occurrence of branch instructions.
  The branch instruction breaks the normal sequence of the instruction stream, causing difficulties in the operation of the instruction pipeline.
  A branch or interrupt instruction changes the PC and makes the fetch of the next instruction to be delayed.

## Slide 29: EXAMPLE OF BRANCH HAZARDS
Clo
Instru
A Bran instruc
Fetch instruction
from memory
Decode instruction and calculate effective address
Branch?
Fetch operand from memory
Execute instruction
Interrupt?
Interrupt
handling
Update PC
Empty pipe
no
yes
yes
no
Segment1:
Segment2:
Segment3:
Segment4:
Consider a 4-Segment Pipeline
FI: Fetch an instruction from memory
DA: Decode the instruction and calculate the effective address of the operand
FO: Fetch the operand
EX: Execute the instruction
ck Cycles |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | 1 | FI | DA | FO | EX |  |  |  |  |  |  |  |  | 
ctions 2 ch  3 tion 4 |  |  | FI | DA | FO | EX |  |  |  |  |  |  |  | 
 |  |  |  | FI | DA FI | FO Stall | EX Stall | FI | DA | FO | EX |  |  | 
5 |  |  |  |  |  |  |  |  | FI | DA | FO | EX |  | 
6 |  |  |  |  |  |  |  |  |  | FI | DA | FO | EX | 
7 |  |  |  |  |  |  |  |  |  |  | FI | DA | FO | EX

## Slide 30: HOW TO AVOID BRANCH HAZARDS?
Prefetch Target Instruction
Fetch instructions in both streams, branch untaken and branch taken
Both are saved until branch is executed. Then, select the right instruction stream and discard the wrong stream
Delayed Branch
Compiler detects the branch and rearranges the instruction sequence by inserting useful instructions that keep the pipeline busy
in the presence of a branch instruction
Branch Prediction (Speculation)
Guessing the branch condition, and fetching an instruction stream based on
the guess.
For example, we may speculate on the outcome of a branch, to implement “delayed branch” so that instructions after the branch could be executed earlier.

## Slide 31: EXCEPTION HANDLING
Exception: An unscheduled or unexpected event that disrupts program execution by changing the normal flow of instruction execution.
  Events other than branches and jumps which may not be predicted.
  Come from within the processor, such as arithmetic overflow.
Interrupt: An exception that comes from outside of the processor, such as an I/O device request
A pipelined implementation treats exceptions as another form of control hazard.
  For example, suppose there is an arithmetic overflow in an add instruction.
Just as we did for the taken branch in branch hazards, we must flush the instructions that follow the add instruction from the pipeline and begin fetching instructions from the new address.