## Slide 1: CS361: Computer Architecture
CS324 Computer Architecture 1
Instruction-level Parallelism
Hazards continued..
RISC Architecture
Book Computer Architecture: A Quantitative Approach, Sixth Edition, Section C.1 – C2 3.1,.3.2,3.3

## Slide 2: BRANCH HAZARDS
A branch (or interrupt) instruction can be conditional or unconditional.
  An unconditional branch always alters the sequential program flow by loading the program counter (PC) with the target address.
  In a conditional branch, the control selects the target instruction if the condition is satisfied or the next sequential instruction if the condition is not satisfied.
» Branch target address is not known until the branch instruction is executed.
One of the major problems in operating an instruction pipeline is the occurrence of branch instructions.
  The branch instruction breaks the normal sequence of the instruction stream, causing difficulties in the operation of the instruction pipeline.
  A branch or interrupt instruction changes the PC and makes the fetch of the next instruction to be delayed.

## Slide 3: EXAMPLE OF BRANCH HAZARDS
Fetch instruction
from memory
Decode instruction and calculate effective address
Branch?
Fetch operand from memory
Execute instruction
Interrupt?
Interrupt
handling
Update PC
Empty pipe
no
yes
yes
no
Segment1:
Segment2:
Segment3:
Segment4:

## Slide 4: HOW TO AVOID BRANCH HAZARDS?
Prefetch Target Instruction
Fetch instructions in both streams, branch untaken and branch taken
Both are saved until branch is executed. Then, select the right instruction stream and discard the wrong stream
Delayed Branch
Compiler detects the branch and rearranges the instruction sequence by inserting useful instructions that keep the pipeline busy
in the presence of a branch instruction
Branch Prediction (Speculation)
Guessing the branch condition, and fetching an instruction stream based on
the guess.
For example, we may speculate on the outcome of a branch, to implement “delayed branch” so that instructions after the branch could be executed earlier.

## Slide 5: EXCEPTION HANDLING
Exception: An unscheduled or unexpected event that disrupts program execution by changing the normal flow of instruction execution.
  Events other than branches and jumps which may not be predicted.
  Come from within the processor, such as arithmetic overflow.
Interrupt: An exception that comes from outside of the processor, such as an I/O device request
A pipelined implementation treats exceptions as another form of control hazard.
  For example, suppose there is an arithmetic overflow in an add instruction.
Just as we did for the taken branch in branch hazards, we must flush the instructions that follow the add instruction from the pipeline and begin fetching instructions from the new address.

## Slide 6: RISC RECAP
Two types of architectures:
  Complex Instruction Set Computer (CISC)
  Instructions can act directly on memory addresses
» For example,
ADD L1, L2, L3
that takes the contents of M[L3] adds it to the contents of M[L2] and stores the result in location M[L1]
  Potentially very long instruction execution cycle (i.e. high CPI)
  Reduced Instruction Set Computer (RISC)
» Load and Store for communication between memory and CPU
» All other instructions are executed within CPU without referring to memory
» All data manipulation instructions have register to register operations.

## Slide 7: RISC RECAP
RISC Program Example:
X = (A + B) * (C + D)
LOAD | R1, A
LOAD | R2, B
LOAD | R3, C
LOAD | R4, D
ADD | R1, R1, R2
ADD | R3, R3, R4
MUL | R1, R1, R3
STORE | X, R1

## Slide 8: RISC PIPELINE
These simple properties of RISC lead to simplification in the implementation of “efficient” pipelining
  The simplicity of the RISC instruction set can be utilized to implement an instruction pipeline using a small number of suboperations, with each being executed in one clock cycle.
During data manipulation, since all operands are in registers, there is no need for calculating an effective address or fetching of operands from memory.
Therefore, the RISC instruction pipeline is mostly implemented with three segments:
  Segment 1: Fetches the instruction
  Segment 2: Decode and executes the instruction in the ALU
  Segment 3: Store the result

## Slide 9: RISC PIPELINE
Instruction Cycles of Three Segment Pipeline
Load and Store Instructions
I: Instruction Fetch
A: Decode, Evaluate Effective Address
E: Register-to-Memory or Memory-to-Register
Data Manipulation Instructions
I: Instruction Fetch
A: Decode, Read Registers, ALU Operations E: Write a Register
Program Control Instructions
I: Instruction Fetch
A: Decode, Evaluate Branch Address E: Write Register(PC)
RICS pipelining benefits from complier based handling of hazards, such as
delayed load and delayed branch.